## Slide 1
UNIT 1
First programs

## Slide 2: Aim and Agenda of unit 1
Create some initial programs that enable you to work quickly and easily with digital input and output (I/O). We will have a look at the basic statements you need to use digital input and output;
Explain what a program looks like
Present program staments
Logic operators
The aim of the presentation
The agenda of the presentation
2

## Slide 3
WHAT A PROGRAM LOOKS LIKE
3

## Slide 4
COMMENTARY SECTION
  All programs should begin by supplying certain information
  This information is called the “Header Comments”
  You can include all the comments you want wherever you want as long as they appear between the symbols “/*” and “*/”
WHAT A PROGRAM LOOKS LIKE
4
1

## Slide 5
VARIABLE AND FUNCTION DECLARATION
  Use this second section to declare variables and functions
  Think of a variable as a kind of box or receptacle you assign a name and possibly a value to
  Generally speaking, both the variables and the functions must be declared BEFORE being used in the program.
WHAT A PROGRAM LOOKS LIKE
5

## Slide 6
CONFIGURATION TASK
  Programs written in Arduino language begin by executing a few configuration instructions or functions.
  Generally speaking, the configuration statements or functions are only executed once when you RESET the system or connect it to a power source.
WHAT A PROGRAM LOOKS LIKE
6

## Slide 7
MAIN BODY OF THE PROGRAM
  You have to write all the instructions, statements and functions that make up your program in this section
  The controller executes all the functions that make up the main body of the program as fast as possible. It executes them constantly and indefinitely from first to last.
  Important: When declaring the variables and configuration and main program functions, make sure they ALWYS end with this symbol: “;”.
WHAT A PROGRAM LOOKS LIKE
7
4

## Slide 8
MESSAGES SECTION
  It will tell you whether you’re saving, compiling or recording a program on the controller’s memory
  It’ll also let you know if there have been compilation errors, the type of error and where they have occurred.
  “Compile” a program means to translate the one you’ve written using complex Arduino language into binary code (also known as machine language); this is what is actually recorded on the controller’s FLASH memory
WHAT A PROGRAM LOOKS LIKE
8

## Slide 9
  The setup() Function
      This function and all the other functions contained in it are ONLY executed when the system is reset
      There are usually a number of other functions within this one: input and output pin configuration, certain variable settings, libraries etc.
      You can put whatever statements and functions you like in the setup() function as long as they are enclosed by curly braces: “{...}”
PROGRAM STATEMENTS
9
Syntax:
Void setup()
{
.......
}

## Slide 10
  The PINMODE() Function
      Configure one of the Arduino controller’s pins as an input or an output
      It usually comes at the beginning of a program and is included in the setup() function
      All the digital pins are automatically configured as inputs when you reset the system.
PROGRAM STATEMENTS
10
Syntax:
pinMode(pin,mode);
pin: This is the number of the pin we’re going to configure; it may be between 0 and 13 in Arduino Mode: This establishes whether it functions as an INPUT or OUTPUT

## Slide 11
  The digitalread() Function
      This function reads and returns the binary logic state (“1” or “0”, “HIGH” or “LOW”) of any of the Arduino controller pins
PROGRAM STATEMENTS
11
Syntax:
digitalRead(pin);
pin: This displays the number of the pin we’re going to read; it may be between 0 and 13 in Arduino

## Slide 12
  The digitalwrite() Function
      Writes or sets a binary value (“1” or “0”, “HIGH” or “LOW”) through an output pin
PROGRAM STATEMENTS
12
Syntax:
digitalWrite(pin, value);
pin: This displays the number of the pin we’re going to read; it may be between 0 and 13 in Arduino
Value: Indicates the value to be set (“1” or “0”, “HIGH” or “LOW”).

## Slide 13
  The not operator
      This operator expresses a negation (NOT) and is represented by an exclamation mark (!)
Logical operators
13
Example:
Value = ! digitalRead(12);
Value equals level 1 if  pin12 is at level 0
Value equals level 0 if  pin12 is at level 1

## Slide 14
Logical operators
14
Example:
Value =digitalRead(4) && digitalRead(8) && digitalRead(12);
Value equals level 1 if  pins 4,8 and 12 are at level 1
Value equals level 0 if  pins 4,8 or 12 are at level 0
  The AND operator
      This operation generates a level “1”, also known as “true”, when ALL the elements that you relate to each other are also at level “1”
      It’s represented by these symbols: “&&”

## Slide 15
Logical operators
15
Example:
Value =digitalRead(4) || digitalRead(8) || digitalRead(12);
Value equals level 1 if  pins 4,8 or 12 are at level 1
Value equals level 0 if  pins 4,8 and 12 are at level 0
  The or operator
      This operation generates a level “1”, also known as “true”, when ANY of the elements that you relate to each other are also at level “1”
      It’s represented by these symbols: “||”

## Slide 16
Logical operators
16
Example:
Value = (digitalRead(8) && ! digitalRead(12)) || digitalRead(4));
Value equals level 1 if  pin 8 is at level 1 and pin 12 is at level 0 or pin 4 is at level 1
Value equals level 0 if  pin 8 is at level 0 or pin 12 is at level 1 and pin 4 is at level 0
  COMBINING operatorS
      You can of course combine various logic operators in the same function
      You have to use parentheses to establish the order they have to be assessed and calculated

## Slide 17
UNIT 1: First programs
Thank You