## Slide 1
UNIT 3
EXPRESSIONS, PAUSES AND SOUNDS

## Slide 2: Aim and Agenda of unit 3
Take a closer look at variables, constants and expressions in general.
Introduce you to some new functions from the Arduino programming language to create pauses and sounds
Present what kind of expressions we could use with Arduino
Give the basic functions for use pauses
Give the basic functions for use sounds
The aim of the presentation
The agenda of the presentation
2

## Slide 3
Arduino language functions you’ve studied until now
EXPRESSIONS
3
pinMode(pin, mode): you have to specify the number of the pin you’re referring to and whether it’s an input or an output.
digitalRead(pin): you have to specify which number pin you want to read.
digitalWrite(pin,value): you have to specify which number pin you want to use to establish the value.
You can express these parameters in different ways
Constant: digitalRead(4) reads the value of input pin number 4.
Variable: digitalRead(pushbutton), reads the input pin defined in the “pushbutton” variable.
Operation:, digitalRead((1+1)*2) reads pin 4 as this is the result of (1+1)*2.

## Slide 4
CONSTANTS
    A program value that never changes may be used as a “constant”
    There is NO way of changing this during the execution of the program
    If you decide to change it you have to modify the program and record it again onto the controller’s memory
    They are stored in the controller’s FLASH memory program
    They are not volatile and even when the power is disconnected they maintain their value
EXAMPLES
EXPRESSIONS
4
digitalRead(12); //read input pin 12
digitalWrite(6,HIGH); //set output pin 6 on level “1”
pinMode(9,OUTPUT); //Configure pin 9 as an output

## Slide 5
VARIABLES
    Are spaces in the controller’s RAM memory specially designed for storing different kinds of data
    You can read and write the RAM memory as much as you want as long as you do it the right way
EXAMPLE
EXPRESSIONS
5
type name = value
type: Establishes the type of data that the variable contains
name: This is the name you assign to the variable or container
value: This is the content or value we put in the variable

## Slide 6
Following table contains a summary of the most common types of variables
EXPRESSIONS
6
TYPE | BYTES | DESCRIPTION
char | 1 | A char takes up 1 byte of memory and stores a character value (8 bits). Character literals are written in single quotation marks (‘).The char datatype is a signed type, meaning that it encodes numbers from -128 to 127.
byte | 1 | A byte stores an 8-bit unsigned number and yields a range of 0 to 255 (28-1).
int | 2 | Integers are your primary data-type for number storage. They store a signed 16-bit (2-byte) value and yield a range of -32768 to +32767
unsigned int or word | 2 | Stores an 16-bit unsigned number and yields a range of 0 to 65535 (216-1)
long | 4 | These are signed variables that store 32 bits (4 bytes) and yield a range of -2,147,483,648 to 2,147,483,647.
unsigned long | 4 | Unsigned variable that stores 32 bits (4 bytes) and yields a range of 0 to 4,294,967,295 (2^32 - 1).
float | 4 | Floating-point numbers can be as high as 3.4028235E+38 and as low as -3.4028235E+38. They are stored as 32 bits (4 bytes) of information.

## Slide 7
“Arrays” are another kind of variable
    An array is a group of variables and it may comprise any of the ones in the above table
    To access the contents of the variables you have to indicate their index number
EXPRESSIONS
7
Variables may be “global” or “local” depending on where you declare them in the program
    Globals: These are the variables that are declared or defined outside all the functions in the program including setup() and loop()
    Locals: These are the variables that are declared and created within a certain function and may only be used by that function

## Slide 8
OPERATIONS
    The values you load into the variables can be obtained as a result of doing all sorts of arithmetic operations between variables and/or constants.
EXPRESSIONS
8
These are the most common mathematical operations
= Equivalence
+ Addition
- Subtraction
* Multiplication
/ Division
% Remainder (the remainder of a division between two whole numbers)

## Slide 9
It’s often a good idea for the controller to do absolutely nothing useful or, in other words, for it to waste a bit of time.
Arduino programming language has a number of functions that pause the execution of a program for a set amount of time
TIMINGS
9
DELAYMICROSECONDS() FUNCTION
    Pauses the program for the amount of time (in microseconds) specified
    delayMicroseconds(n);
    n: indicates the number of milliseconds you want to pause the program. It’s a 16 bit unsigned integer
EXAMPLE
A = 100;
delayMicroseconds(A); //pauses the program for 100 µS = 0.1 mS = 0.0001 seconds

## Slide 10
EXPRESSIONS
10
DELAY() FUNCTION
    Pauses the program for as many milliseconds as you indicate
    delays(n);
    n: indicates the number of milliseconds (mS) you want to pause the program. These are referred to as long numbers without a 32 bit sign or unsigned long numbers
    EXAMPLE
A = 100;
delay (A); //Pauses the program for 100 mS = 0.1 second delay(1000)

## Slide 11
EXPRESSIONS
11
MICROS() FUNCTION
    Returns the number of microseconds elapsed since Arduino began running your program
    It returns an unsigned long value and the number will overflow (go back to zero) after approximately 70 minutes
    var = micros();
    var: This is the variable that stores the microseconds (µS) elapsed since the system was restarted.
MILLIS() FUNCTION
    Returns the number of milliseconds (mS) elapsed since Arduino began running your program
    It returns an unsigned long value and the number will overflow (go back to zero) after approximately 50 days
    var = micros();
    var: This is the variable that stores the milliseconds (mS) elapsed since the system was restarted.

## Slide 12
What do you need to create sound?
SOUND
12
A device able to vibrate and produce pressure changes or vibrations in the air
These vibrations reach our ear drums and our brain perceives them as sound
There are lots of well known devices that cause changes in the air pressure and thus create waves that carry sound: loud speakers, headphones, buzzers, sirens
Humans are able to hear sound frequencies between approximately 20 Hz and 20,000 Hz (20 KHz) or cycles per second. This indicates the frequency or number of times per second a signal passes from “1” to “0”.

## Slide 13
Arduino programming language makes it very easy for you to produce all sorts of sounds
  All you have to do is indicate the F frequency and Arduino will take care of the rest.
TONE() FUNCTION
  Generates a sound with the required F frequency on the output pin and for the duration indicated.
  tone(pin, frequency, duration);
  pin: indicates which pin you’re going to generate the sound on.
  frequency: represents the frequency of the tone in Hz (hertz).
  duration: This parameter is optional. It’s an unsigned long number that represents the duration of the tone in milliseconds
SOUND FUNCTIONS
13

## Slide 14
noTONE() FUNCTION
  Stops a tone on a designated pin
  tone(pin);
  pin: represents on which pin the sound is going to be stopped.
  EXAMPLE:
SOUND FUNCTIONS
14
tone(2,13000); //Generates an indefinite tone 13 KHz tone on pin 2.
…. //The tone keeps sounding.
noTone(2); //The tone stops.

## Slide 15
UNIT 3 EXPRESSIONS, PAUSES AND SOUNDS
Thank You