## Slide 1
UNIT 4
Decision making and control functions

## Slide 2: Aim and Agenda of unit 4
Study the functions that control the flow and execution of a program
Study comparison, Boolean and compound operators
Present different kind of sequentially functions
  If () function
  If() else function
  For() function
  While() function
Present different kind of control functions
The aim of the presentation
The agenda of the presentation
2

## Slide 3
Arduino knows how to make comparisons between numbers or the results of certain functions.
Here are the various comparison operators as well as the signs that represent them
COMPARISON OPERATORS
3
OPERATOR | SIGN | OPERATOR | SIGN
Equal to | = = | Different to | !=
Less than | < | Greater than | >
Less than or equal to | < = | Greater than or equal to | >=

## Slide 4
It’s even possible to relate some of preceding comparisons to each other
There are also only two possible results when two or more expressions are related using these logical operators: “true” o “false”.
BOOLEAN OPERATORS
4
OPERATOR | SIGN
NOT | !
AND | &&
OR | ¦¦
(Letter == ‘X’) && (A > 10) //False
(A == 10+3) && (B >= 12345) && (Letter != ‘Q’) //True
(B > 12300) || (PI = 3.1412) //True
(A == B) || (A > 10 + 4) //False
!(A == B) //True
EXAMPLES

## Slide 5
Lots of times you’ll be doing very simple operations with a variable and the result will end up in the same variable.
Remember that you can use the so-called “compound operators” to simplify these expressions
COMPARISON OPERATORS
5
OPERATION | OPERATOR | EXAMPLE | EQUAL TO
++ | increases a unit | X++ | X= X + 1
- - | decreases a number | Y- - | Y = Y - 1
+ = | addition | X+=Y | X = X + Y
-= | subtraction | X-= 3 | X = X - 3
*= | multiplication | X *= Y | X = X * Y
/= | division | X /= 5 | X = X / 5

## Slide 6
IF() FUNCTION
  This is the most basic and important control function
  If the result is “true” it executes all the functions inside the curly braces “{…}”. If the result is “false” the controller doesn’t execute them and the program keeps going.
CONTROL FUNCTION
6

## Slide 7
IF() FUNCTION
CONTROL FUNCTION
7
if(expression)
{
….
}
expression: establishes the condition that the Arduino controller has to assess.
curly braces: they might look like the two slices of bread in a sandwich
EXAMPLE:
void loop()
{
if((A>B) || (C < 25)) //If the condition is true…
{
digitalWrite(6,HIGH); //Switches on pin 6
C=25; //A value of 25 is stored in the C variable
}
.... //Continues the execution....
}

## Slide 8
IF() ELSE FUNCTION
  it’s a derivative of the previous if(…) function
  If it’s “true”, all the functions in the curly braces “{…}” are executed just the same as with the if(…) function.
  If the condition is “false” all the functions enclosed by the else {…} braces are executed. Once the functions have been executed, whether or not the condition is true or false, the program keeps going
CONTROL FUNCTION
8

## Slide 9
IF()ELSE FUNCTION
CONTROL FUNCTION
9
if(expression)
{
….
}
else
{
….
}
expression: establishes the condition that the Arduino controller has to assess.
curly braces: they might look like the two slices of bread in a sandwich
EXAMPLE:
if(digitalRead(4) == 1) //If pin 4 is on “1” …
{
digitalWrite(6,HIGH); //Enables pin 6
}
else //…and if not…
digitalWrite(6,LOW); //Disables output 6
…. //Continues executing the program

## Slide 10
FOR() FUNCTION
  This function enables us to create controlled loops
      We declare an initial value
      The value variable is changed automatically
      If it's true, the statement block and the increment are executed and then the condition is tested again
      When the condition becomes false, the loop ends
CONTROL FUNCTION
10

## Slide 11
FOR() FUNCTION
CONTROL FUNCTION
11
for(initialization,condition,increment)
{
….
….
}
initialization: makes it possible to establish the value of a variable
condition: it’s the condition that’s tested
increment: makes it possible to change the value of the variable
curly braces: they might look like the two slices of bread in a sandwich
EXAMPLE:
for (int N = 1; N < 5; N=N+1) //Establishes the loop conditions
{
digitalWrite(6,HIGH); //Enables pin 6
delay (150); //Pauses the program for 0.15”
digitalWrite(6,LOW); //Disenables pin 6
delay (1000); //Pauses the program for 1”
}
…. //Continues executing the program

## Slide 12
WHILE() FUNCTION
  While loops are a variation on for() functions
  They are also used for loops where a group of functions are executed a certain number of times
  while(condition)
  {
  ….
  ….
  }
  condition: this is the conditional expression. It will loop continuously, and infinitely, until the expression inside the curly braces, {}, becomes false. When it does, the loop finishes and the program keeps going.
CONTROL FUNCTION
12

## Slide 13
CONTROL FUNCTION
13
WHILE() FUNCTION
  EXAMPLE:
  int N = 6 while (N > 0) //While N is greater than 0
  …
  {
  digitalWrite(6,HIGH); //Enables pin 6
  delay (150); //Pauses for 0.15”
  digitalWrite(6,LOW); //Disenables pin 6
  delay (1000); //Pauses for 1”
  n--; //The next value for N ( N = N – 1)
  }
  ….
  …. //Continues executing the program

## Slide 14
  This function will enable you to choose between several “ways” of executing various groups of functions
  A switch statement compares the value of a variable to the values specified in case statements
  “If the value of the variable is X do these functions. If the value of the variable is Y do these other ones. If it’s Z do these other ones etc…”
SWITCH() / CASE FUNCTION
14

## Slide 15
SWITCH() / CASE FUNCTION
15
switch(variable)
{
case X:
….;
break;
case n:
….;
….;
break;
default:
….;
}
variable: this is the value of the variable that’s going to be compared with the ones in each “case” mentioned.
case: this fixes all the values that are going to be compared to the contents of the variable.
default: this is optional. If none of the values coincides all the functions are executed.

## Slide 16
CONTROL FUNCTION
16

## Slide 17
OTHER CONTROL FUNCTIONS
17
DO…WHILE() FUNCTION
The do loop works in the same way as the while() loop, with the exception that the condition is tested at the end of the loop
        do
        {
        ….
        } while(condition)
RETURN FUNCTION
This one terminates a function and returns a value from any function created by the user to the calling function.
        return;
        return value;
value: this is the value the function returns when it goes back to the calling program
BREAK FUNCTION
break is used to exit from a for(),while() or do() loop, bypassing the normal loop condition. It is also used to exit from a switch() / case statement
        break;
GO TO() FUNCTION
Transfers program flow to a labelled point in the program.
        test:
          ….
        goto test:
Jumps to wherever the label indicated.

## Slide 18
UNIT 4 Decision making and control functions
Thank You